## Slide 1: IoT Automation and Data Transmission through MQTT Broker in Node Red
Dr.V.Berlin Hency
Associate Professor
SENSE
VIT Chennai

## Slide 2: Objective
MQTT
JSON
MOTT In node and MQTT Out Node Properties
Sample flow with MQTT Broker – Debug Monitor
MQTT publish data in UI interface

## Slide 3: MQTT
Message Queuing Telemetry Transport Protocol
Light weight protocol
Bandwidth efficient
Little Battery power
Uses Publish /Subscribe Architecture

## Slide 5: MQTT

## Slide 6: Example

## Slide 7: Application

## Slide 8: JSON-Java script Object Notation
JSON is a language independent lightweight data interchange format
JSON is text
We can convert any JavaScript object into JSON and easy to send JSON to the server
While exchanging data between a browser and a server the data can only be text for easy transmission

## Slide 9: Connecting to an MQTT Broker to Server
To connect to an MQTT broker or server, need to know
  The Broker IP address or name
  The port address (Default 1883)
In addition a client needs to provide
  A client name to identify itself
  ie each client connection requires a unique client name

## Slide 10: Flag and Parameter
Flag/Parameter that the client can set are
  Clean Session Flag
  Time to Live

## Slide 11: Clean Session Flag
MQTT clients by default establish a clean session with a broker.
A clean session is one in which the broker will not remember anything about the client when it is disconnected.
With a non clean session the broker will remember client subscriptions and may hold undelivered message for the client.

## Slide 12: Time to Live
The mechanism used to determine whether a connection is still alive
The default interval is 60 seconds

## Slide 13: Publishing using the publish Node
While client publishes a message to boker it needs to send
  The message topic
  The message QoS
  Retain flag ( Whether the message should be retained.default : False,If “True” then last message will be retained)

## Slide 14: QoS
QoS 0- Once
  Message delivered once or not ;not guaranteed
QoS 1- At least once
  Message delivered atleast once or more times and quaranteed
  The message will continue to be resent at regular intervals until the sender receives the ack
QoS 2 Only Once
  Guaranteed
  Slow, both receiver and sender sends ack

## Slide 15: MQTT hosting Providers
Cloudmqtt
Flespi
Myqtthub.com
Beebotte
Mosquitto
HiveMQ
mosca

## Slide 16: Online Cloud Base MQTT Brokers/Servers
Broker Type | Broker Address and Port
Mosquitto | test.mosquitto.org and 1883
HiveMQ | broker.hivemq.com and 1883
Mosquitto | iot.eclipse.org
mosca | test.mosca.io and 1883

## Slide 17: MQTT Server
Server : broker.mqttdashboard.com
Port : 1883

## Slide 18: Node red MQTT Publish subscribe nodes
Common connection settings for both publish and subscribe

## Slide 19: Configuration of MQTT Publish and Subscribe Nodes in node red
Node Red Provides
  MQTT input – Subscribe Node
  MQTT Output – Publish Node

## Slide 20: Command Prompt
Cmd (Go to command prompt)
Node-red –v (to trigger node red)
http://127.0.0.1:1880/

## Slide 21: Part A
To display RFID Reader content to Node Red Debug window using HiveMQ (MQTT Broker)

## Slide 22: To Disable previous flow if any

## Slide 23: Configure MQTT in Node

## Slide 29: HiveMq
http://www.hivemq.com/demos/websocket-client/

## Slide 30: Click Connect

## Slide 31
{"Name":"BERLIN","Organization": "VIT","EmpID":50619}

## Slide 33: Insert json node and debug node and wire

## Slide 34
Deploy

## Slide 35: Click Publish

## Slide 36: Output in Node red Debug Window

## Slide 37: PART B
To Display Bike speed to Node Red Dashboard using HiveMQ (MQTT Broker)

## Slide 38: Configure MQTT in -Speed Sensor

## Slide 43
Insert Debug node Slider node gauge node
And text input node

## Slide 45: Configure Guage node

## Slide 47: Configure Slider node

## Slide 49: Configure Text Input Node

## Slide 51
Deploy

## Slide 52
http://www.hivemq.com/demos/websocket-client/

## Slide 53: Click Publish

## Slide 54
http://127.0.0.1:1880/ui

## Slide 56: MQTT Out Node
Refrigerator automation
  Insert 3 inject nodes
  Insert one MQTT Out node
  Insert One Debug node
  Wire All nodes

## Slide 62: Config MQTT Broker

## Slide 64
http://www.hivemq.com/demos/websocket-client/

## Slide 65: Click Connect

## Slide 66: Click add New topic subscription

## Slide 69
Deploy
Trigger inject Node

## Slide 71: Reference
http://www.steves-internet-guide.com/configuring-the-mqtt-publish-node/